M/V SWARD EX RIMEO

IMO Nr:8324713

BUILT: 1984 Germany Schlichting Werft

DWT:11127mt  DRAFT: 8,279m

CLASS: VRS

GRT/NRT:8183 / 4408

LOA: 135,07  BREADTH: 20,60M DEPTH :11M

H/H: 3/3 GRAIN / BALE :14387,2 m3 /14200 m3

GEARED  bss Cranes capable to lift every single coil of c/p cargo

M/E MAN B&W 8L 40/45 medium speed coupled to gearbox and 4.50m diam variable pitch prop.

MCR 4840 kw,6600ps 600 Rpm (prop Esher Wyss 4 blade right turning)

A/E 2 X Volvo Penta DG 16 450 KW 1500 rpm with Volvo Emg. DG 135 kW

1 Shaft Alternator 690 KVA,550 kW

Speed 11k , cons 11.0t ifo 380

Bow Thruster: Jastram 441KW 600PS